## Slide 1
Cyclic Queuing and Forwarding with tagging for Deterministic Forwarding draft-eckert-detnet-tcqf-02 draft-yizhou-detnet-ipv6-options-for-cqf-variant-01
Toerless Eckert, Futurewei USA (tte@cs.fau.de), Yizhou Li <liyizhou@huawei.com> Stewart Bryant, U. of Surrey ICS (s.bryant@surrey.ac.uk), Andy Malis (agmalis@gmail.com), Guangpeng Li <liguangpeng@huawei.com>, Shoushou Ren <renshoushou@huawei.com>, Guangpeng Li <liguangpeng@huawei.com>, Fan Yang <shirley.yangfan@huawei.com>, Jeong-dong Ryoo <ryoo@etri.re.kr>, Peng Liu <liupengyjy@chinamobile.com>
Interim meeting 04/2023, rev 0.6
https://github.com/toerless/detnet/blob/main/tcqf-slides.pptx

## Slide 2: Draft work -02 (IETF116) to -03
Detailled presentation of mechanism from draft-eckert-detnet-tcqf-02 and draft-yizhou-detnet-ipv6-options-for-cqf-variant-01 at DetNet interim
  Slides, recording see DetNet interim Wiki: https://wiki.ietf.org/en/group/detnet/wmosq
  David raised question / possibility to merge.
-03 performed merge of content/authors
Detailed explanation of evolution from CQF to TCQF
  CQF model, timing, challenges: buffer ambiguity upon reception
  Solution with TCQF (tagging of packet), timing, summary of TCQF benefits
  Appendix: Discuss of IEEE “Multiple Buffer CQF” (without tagging) and how it (in our option) does not meet our requirements
Made forwarding specification independent of encap
  Separate sections now for (non-exhaustive) encap options:
  From -02: MPLS/TC, IP/IPv6 with DSCP
  New IPv6 option header for TCQF “Deterministic IP” (DIP) option via 2 possible extension header alternatives), IANA considerations for it.

## Slide 3: Draft independent
Translation of CENI “Deterministic IP” (DIP = TCQF) high-speed/large-scale network validation test report
  We used slides from mandarin version in our IETF116 presentation
Now available with permission from CENI at:
  https://github.com/network2030/publications/blob/main/ CENI_DIP_Networking_Test_Report.pdf
Also referenced in current draft.

## Slide 4: Draft work -03 to -04
Following presentation of CSQF at DetNet interim
  Draft-chen-detnet-sr-based-bounded-latency, See Detnet wiki for recording/slides
Added appendix comparing TCQF/CSQF
  CSQF moves hop-by-hop cycle mapping to packet metadata (Segment Routing SIDs).
  Mostly subtle pro/cons for either option – best explored through deployment experience.
  Any hardware can easily support both TCQF and CSQF.
  Operator preference will be most important: CSQF is “SR version of TCQF”.
  CSQF key additional functional benefit (not well quantified yet) in “frame-interleaving”. Discussed in new draft. (“better burst management”).
After another review of CQF in IEEE spec:
  CQF could support multiple independent instances of cycle buffers
    selected by e.g.: packet priority.
  Same could be done in TCQF
  No evidence that we need this (CSQF for example is simpler), but want to make sure IEEE experts understand that – if needed - TCQF solution could support all options that CQF could.

## Slide 5: Status / Open issues ?
Draft is quite complete, has received significant review/validation.
Other desirable DetNet components, such as “gates” would be beneficial in conjunction with TCQF:
  See draft-eckert-detnet-frame-interleaving
But should be considered independent from hop-by-hop-forwarding
  Same as e.g.: PREOF functions are also complementary to hop-by-hop forwarding but kept architecturally separate.