## Slide 1: CENI TCQF (“DIP”) Testbed 2020
Test Engine
DIP
Router
Beginning
Target Flow：1Packet/10μs & pktsize is 1500B
Interference flow：128Packets/1ms & pktsize is 1500B
Transit
back
Shanghai
Taizhou
Yangzhou
Equipment Room in NanJing
DIP
Router
1200km Geo Distance
10Gbps Fiber
Taizhou
Shanghai
Yangzhou
NanJing

## Slide 2: DIP test result of the Beijing-Nanjing 1k+ km loopback network
The number of interference flows | End-to-End delay of Non-DIP (μs) |  |  |  | End-to-End delay of DIP (μs) |  |  | 
 | Min | Ava | Max | Max Jitter | Min | Ava | Max | Max Jitter
1 | 27142 | 27146 | 27196 | 54 | 27176 | 27195 | 27205 | 29
2 | 27142 | 27152 | 27513 | 371 | 27176 | 27195 | 27205 | 29
3 | 27142 | 27162 | 27831 | 689 | 27176 | 27195 | 27205 | 29
4 | 27142 | 27211 | 28148 | 1006 | 27176 | 27195 | 27205 | 29
5 | 27142 | 27269 | 28466 | 1324 | 27176 | 27195 | 27205 | 29
6 | 27142 | 27338 | 28784 | 1641 | 27176 | 27195 | 27205 | 29
7 | 27143 | 27338 | 29102 | 1959 | 27176 | 27195 | 27205 | 29
8 | 27143 | 27444 | 29322 | 2179 | 27176 | 27195 | 27205 | 29
9 | 27143 | 27601 | 29545 | 2402 | 27176 | 27195 | 27205 | 29
10 | 27143 | 27713 | 29766 | 2623 | 27176 | 27195 | 27205 | 29
11 | 27143 | 27827 | 29989 | 2846 | 27176 | 27195 | 27205 | 29