## Slide 1
Cyclic Queuing and Forwarding for DetNet IP and MPLS Data Plane (TCQF)
...and BIER-TE... draft-eckert-detnet-tcqf-01
Toerless Eckert, Futurewei USA (tte@cs.fau.de)
Stewart Bryant, University of Surrey ICS (s.bryant@surrey.ac.uk)
Andy Malis (agmalis@gmail.com)
Guangpeng Li <liguangpeng@huawei.com>
IETF DETNET WG, IETF115, 11/07/2022, rev 1.1

## Slide 2: Scalability in large DetNets
Realistic reference worst case scenario in large-scale DetNet
  Assume we aggregate all DetNet traffic from one ingres iPEj to one egres ePEk into one aggregate DetNet flow.
    Most edge-aggregation we can do
    j=1...100, k=1...100
  Total # flows: j * k = 100 * 100 = 10,000
  These flows may all go through one (core PE) interface
    oif1 (output interface 1) on P1 in example network
RFC2211 (IntServ): per-flow shaping for 10,000 flows
IEEE ATS (Async Traffic Shape): interleaved regulators for 10,000 flows
Every time rate and/or burst-size of any of these 10,000 flows changes (because one of its member flow changes):
  Both IntServ and ATS require signaling of new flow parameters to all routers affected (P1, P2, ...) – (limited optimizations possible).
TCQF: 3 ... 5 cyclic queues on P1 oif1.
  No changes in any P router configuration when member flows change!
iPE100
iPE1
...
ePE100
ePE1
...
P1 rtr
P2 rtr
...
...
oif1

## Slide 3: Scalable traffic steering support
DetNet flows need resource reservation along path
  bandwidth/buffers – shape of traffic depends on queuing mechanism
Result: Standard IGP (re-routing) insufficient
  No resources reserved (immediately) on re-routed path
Standard DetNet expectations
  Explicit route for DetNet flow on every hop (IP 5/6-tuple flow, MPLS label path with RSVP-TE)
  Known scalability, performance issues (RSVP-TE).
  Per-flow, per-hop static routes in IP less well explored (IMHO: worse !)
Solution: “source-routing”: Per-hop, per-flow stateless strict-steering options:
  SR-MPLS, SRv6 (CRH extension header), BIER-TE (multicast)
Without additional flow-id header, stateless solutions could:
  (maybe) identify one iPE->ePE DetNet flow from IP/MPLS header, but:
  Would re-introduce per-iPE/ePE flow, per-hop state that needs to be updated in forarding plane
With stateless steering: One really wants to use a solution like TCQF not requiring to introduce per-hop, per-flow state for queuing.
  TCQF is “natural” match for source-routing in forwarding.

## Slide 4: Overview CQF with packet-tagging of cycle to enable large-scale detnets
Benefits from CQF
  Scalable, low-cost hardware implementable – at > 100 Gbps interfaces routers
    Candidate target: implementable on all programmable forwarding planes supporting CQF
  Bounded Latency with extremely simple latency calculus model
  Tightly bounded jitter – for all existing control-loop applications (industrial etc.)
    Removes need for clock synchronization on constrained DetNet USER-devices
CQF problems solved with TCQF
  Arbitrary (wide-area network) link propagation latency / jitter
  Reduced clock synchronization accuracy requirement
Changes over CQF
  Use multiple buffers
  Use existing packet header field (MPLS TC / IP/IPv6 DSCP) as cycle-tag
  Replace arrival time based cycle use with packet header tag cycle mapping
Can cook coffee

## Slide 5: Changes since IETF114 draft-eckert-detnet-mpls-tc-tcqf-03 -> draft-eckert-detnet-tcqf-00/01
IETF114: draft-eckert-detnet-mpls-tc-tcqf-03
  Described only MPLS support (TC tagging)
    Authors felt IP support with standardized DSCPs would require different IETF process (TSVWG responsibility ?)
  @IETF114, David Black reminded us
    DetNet is controlled domain (single operator or coordinated operations)
    “private” DSCP space has same applicability as MPLS TC here
Resulted in adding text for IP/IPv6 with DSCP tagging
  Simple text enhancements: add DSCP, data model, pseudo-code
  xxxx11 "EXP/LU" Codepoint space according to [RFC2474], Section 6
  Aka: with IP up to 16 DSCP
    not seen significant pre-existing use in my deployment experience (?!)
Text quality improvements, new co-author

## Slide 6: Existing “fields” (DSCP/TC) vs. New header
Goal of this document: First-to-adopt solution
  Most easily first standardized/adopted large-scale-detnet bounded latency
    Existing queuing mechanism (CQF), just with tagging instead of clock-sync
    Existing header fields/private-semantic for tagging – no new packet header stds. work
Longer term work !
  DetNet QoS requiring new header
    IP/IPv6 (extension header): PREOF (sequence-number, ?flow-id?)
    Alternative Marking ? Stream-ID ?
    TCQF (especially MPLS) – more tag values
    Dampers – various mechanisms (with / without cycle buffers): per-hop-latency value
    Heuristic bounded latency parameters (per-hop deadline – Jakov Stein) ?
    Steering together with latency (aka: list of (next-hop, {cycle,deadline,priority,...))
  Same header across IP and MPLS would be ideal ?!
    IPv6 extension header: routing? – IMHO better than HbH (could do QoS AND steer)
    MPLS Design Team work: encap for header shreable with IPv6 ??
  Good solution could be big step for DetNet, but IMHO not fast standardized.

## Slide 7: Summary, Next Steps
Complete “scalable” / large-detnet bounded QoS with low jitter
Most easily adoptable option (?!)
  For both MPLS and IP/IPv6 networks
  Can leverage experience / hardware from CQF / gated queues
  PoC validation via 100Gbps WAN network
Authors / supporters want to ask WG for adoption
Design-team / more regular meeting / work to revisit / collaborate across all posted bounded latency drafts ?
  To validate / work out proposed solution strategy ? (short / long term etc... ?)
  Would be happy to get one started.
Thank you!

## Slide 8: Backup Slide(s)

## Slide 9
Reminder: TCQF High Level
With 3 cycles , arbitrary latency links can be supported
Every node has cycle-mapping table from prior hop (calculated by controller)
Clock accuracy: “Maximum Time Interval Error” (MTIE) < 90% cycle time
With 3 or more cycles, additional inaccuracies can be compensated
e.g.: link propagation variation (jitter) and/or higher MTIE
cycle 1
cycle 2
cycle 3
cycle 1
cycle 2
cycle 3
cycle 1
cycle 2
cycle 1 buffer
sending
sending
cycle 3 buffer
sending
sending
sending
sending
cycle 2 buffer
Node 1 (sender)
Node 2 (“receiver”)
Outgoing interface
cycle 1
cycle 2
cycle 3
cycle 4
cycle 3
cycle 4
cycle 1
cycle 1
cycle 1 buffer
sending
sending
cycle 3 buffer
sending
sending
sending
cycle 2 buffer
cycle 4 buffer
sending
Link propagation latency with variation,
e.g.: Clock drift (MTIE)
Node 1 (sender)
Link propagation latency
Node 2 (“receiver”)