## Slide 1
An information model for Deterministic Data
packets (and beyond ?) draft-eckert-detnet-<tbd>
T. Eckert (Futurewei - tte@cs.fau.de)
DetNet interim meeting 12/2022

## Slide 2: Goals
Large number of deterministic “latency” proposals
  Can/should we standardize all ? How ?
Overview/comparison ?
AFAIK: Can not afford a separate header for each option
  Eg: no hop-by-hop “routing headers in IPv6”
  Forwarding HW would like to have as few headers as possible
  Eg.: Not header for PREOF and another for queuing/latency
    And then we forgot yet another function – third extension header ?
IETF process:
  DetNet can define the function (proof: PREOF) and the information elements needed for it
  Other WGs will likely have to define packetization
  MPLS, 6MAN, ?none-for-IPv6?, ?BIER?
Packet header thinking
  If we need a new header, what other necessary/beneficial packet header fields would we want (latency or other DetNet functions).
Writing up information model
  Helps to separate packetization from functionality
  Should hopefully be a good work item to make progress
  Should be written so that other-WG folks may only need to read what is of interest to them
    Size of information element, where inserted, where examined, read-only vs. read/write,...t

## Slide 3: Information elements (1) – non-latency
IE: Sequence-number
  Functions: IP PREOF, OAM (!), ? new/better MPLS extension header ?
  Format: Is RFC8943 all we need (it was constrained by options of RFC385) ?
IE: Flow-ID
  Functions: Easier OAM/PREOF - avoids per-forwarding plane Flow-key (IP, MPLS, L2)
    Without Flow-ID, OAM functions need to track label binding to know “Flow” (FEC)
  Format: TBD. Example: (sender-id, sender-flow-id) – globally unique

## Slide 4: Information elements (2) – end-to-end
PlayOut Function (in egres DetNet router)
  IE: Playout-TimeStamp
    Set by ingres node based on known max-latency to end node and arrival time of packet.
    Buffers packet on egres node until Playout-TimeStamp.
    Assumes clock synchronization on ingres and egres node
    Allows to use per-hop “jittery” (in-time) QoS (e.g.: rfc2212, TSN-ATS) and convert to “synchronous” (on-time) QoS on egress-node.
  Format:
    Size needs to be larger than maximum network end-to-end latency. 265 msec ?
    Unit of granularity likely depending on network speed ?
    What use-case has highest synchronicity requirement ?
      Audio ? 1 usec ?

## Slide 5: Information elements (3) – hop-by-hop
PlayOut Function (in receiver)
  IE: Accumulated Queuing Delay across path (eDelay)
    Every router adds the latency the packet experienced on this router, frm reception to sending
    On wired networks, no significant external contributors to jitter
      Link-propagation typically well jitter-free ?! (some exceptions)
    Allows network to operate without clock synchronization
      Just require minimum per-router local frequency accuracy (easy to achieve for e.g.: “Ethernet accuracy”)
      No buffering requirements in router – makes it most simple latency support function in routers ?
    Receiver can then use eDelay value for receiver-only playout buffering to
      Buffering/delaying packets on receiver (software) much cheaper than in network ?
  Format:
    Similar to prior slide. E.g.: usec accuracy, max-size < 1 sec -> 24...32 bits.

## Slide 6: Information elements (4) hop-by-hop-latency
IE: “delay” time (not timestamp!)
  Damper Function – makes next node delay packet
  Rewritten every hop
  Size/accuracy depending on how “jitter-free” end-to-end path should be
    And capabilities of forwaders for accurate timing of packets.
    Max accuracy : time of sending 1 bit on fastest interface.
    Size: maximum number of bits in a queue (from maximum latency on hop).
IE: Cycle number
  E.g.: TCQF - Determined cycle buffer on next hop
  Rewritten on every hop
  Similar in function, but much smaller than “delay” parameter (e.g.: 4 bit)

## Slide 7: Information elements (5) per-hop-priority
IE: list of per-hop priority
  Small value, e.g.: 4 bit
  But needs to be a sequence, one value per DetNet hop
  Think of priority in UBS/TSN-ATS
In DetNet with per-flow state, this could be attached to the state of the flow on each DetNet hop – but not with “per-flow stateless forwarding”
  SR-MPLS, SRv6, BIER-TE
Stateless forwarding already has packet header to indicate path (or tree)
  Difficult to imagine that one would want a separate data-structure to indicate per-hop priorities
  Likely: per-hop-priority needs to use/expand existing “steering header”
  SR-MPLS: 16 label/SID per DetNet node (= 4 bits priority)
  SRv6: 4-bit function parameter in SRH. 4 bits per steering hop in TBD CRH header
  BIER/BIER-TE: ? Difficult ?

## Slide 8: Information elements (6) per-hop-deadline
IE: list of per-hop deadlines
  Proposed in e.g.: draft-stein-srtsn
  Currently no deterministic calculus defined, but stochastic with high probabilities
Similar considerations as per-hop priority
  Except granularity
  Possible with e.g.: 32 bits in SRH ?
  Impossible within existing 20-bit SR-MPLS label space ?!
Just example for:
  A per-hop-sequence

## Slide 9: Code points (1)
Re-use DSCP idea
Instead of defining Information elements with fixed semantic
Define “Code-Point” style Information Elements
  Semantic is assigned through configuration
Example, for each DSCP:
    Queue selection, queue-parameters, scheduler parameters for queue, drop parameters for packet (e.g.: RED, PIE,...)
Using SRv6/SRH or SR-MPLS SID/programmability
  is already a form of “code points”
  So lets assume that hop-by-hop parameter (sequences) are using that.

## Slide 10: (Thought) Experiment
Assume we define a DetNet header with the following fields
  If a router supports a particular queuing/latency mechanism: Would these fields be sufficient to support it (by configuring semantic of fields)
  32 bit latency mechanism parameter 1 (read/write)
    Could be self descriptive, e.g.: start with 4-bit type
    Mechanisms could structure it
  32 bit latency mechanism parameter 2 (read/write)
    Could be self descriptive, e.g.: start with 4-bit type
    Mechanisms could structure it
  32 bit for sequence number (read-only hop-by-hop)
  32 bit for flow-id (read-only hop-by-hop)
Could we support all proposal (except for per-hop parameters) ?
  Even if proposal is not standardized
  We would need to allow how to configure in parallel standard and non-standard semantics
  Or some algo might be standardized later.