## Slide 1
Cyclic Queuing and Forwarding for DetNet IP and MPLS Data Plane (TCQF)
...and BIER-TE... draft-eckert-detnet-tcqf-01
Toerless Eckert, Futurewei USA (tte@cs.fau.de)
Stewart Bryant, University of Surrey ICS (s.bryant@surrey.ac.uk)
Andy Malis (agmalis@gmail.com)
Guangpeng Li <liguangpeng@huawei.com>
IETF DETNET INTERIM, 2022-12-12

## Slide 2: Continuing from IETF115
Good Feedback / like of benefits
  Does not require new packet header (fast adoption in industry ?!!)
  Works same for MPLS and IP
  Hopefully/likely ? Can leverage existing CQF queuing hardware (TSN) Just need to add forwarding code to select cyclic queue from existin packet header field
  Low jitter - industrial/”synchronous” traffic use-cases
    Eliminates need for clock-sync on client devices
Feedback from David Black
  Need to refine pseudocode to eliminate unnecessary constraints
    Only packets that arrived in order from same prior hop need to stay in order
    Scheduling of packet otherwise arbitrary – as long as all are sent within cycle time limit
    (Current pseudocode looks as if to imply more oder via “enqueue/dequeue” functions”

## Slide 3: What should queuing document have ? Is TCQF doc a good or bad reference ?
Describe how it fits into DetNet architecture/topology
Configuration Data Model
Textual description of per-hop processing
  And if different ingres/egres processing
Description of calculus to determine latency
Pseudocode
Scalability / performance (high-speed implementation)
...
What else stands in the way of adoption call ?