## Slide 1
Criteria and Assessment for DetNet Services Forwarding Plane Methods
draft-eckert-detnet-criteria-assessment-00
T. Eckert (Futurewei - tte@cs.fau.de)
DetNet interim meeting 2023-03-07

## Slide 2: Goals
Proposal for how we could attempt to define common criteria for different method proposals (currently mostly looking at latency/jitter services forwarding plane methods).
  Not limited to methods for large-scale detnet, but of course started by considering those.
Expand so that each method can best be representing its benefits
  Best done by doing assessments for different methods and proposing enhancements to the assessment critera and/or means to capture them
Assessments could go into proposals.. Or git.. Or google docs..
  TBD. Not looked at this

## Slide 3: Content
Definition / explanation of assessment criteria
2. Example assessment for TCQF
  Because this is the method i could most easily write down)
  Self-Assessments always look great! Also tried to write up some negatives about TCQF (but in general we would best get negatives into assessments by critiques from authors of opposing proposals)
3. Should also do assessment for existing methods. Eg.: UBS from TSN-ATS.
  Maybe (as we think) not appropriate for large scale detnet but certainly desirable to understand/use in conjunction with DetNet over TSN. Might even propose as a native methos (DetNet flow based instead of mapping to TSN flows).
Following two slides show the example assessment

## Slide 4: Example Assessment (1)
4.1. General
4.1.1. Name of the Mechanism: Tagged Cyclic Queuing and Forwarding
4.2. Reference: [I-D.eckert-detnet-tcqf]
4.3. Service Characteristics
4.3.1. Latency guarantee: Bounded (deterministic)
4.3.2. Jitter: on-time (2* cycle-time T)
4.4. Network Applicability
4.4.1. Intended for IP, IPv6 and MPLS networks
4.4.2. Intended for 100Gbps networks and faster
4.4.3. Latency requirements for links: arbitrary
4.4.4. Wireline Jitter: supported (at the cost of higher per-hop
4.4.5. Radio Jitter: NO / TBD
4.5. Node Clocking
4.5.1. Asynchronous: No
4.5.2. MTIE impact on jitter and bounded latency

## Slide 5: Example Assessment (2)
4.6. Traffic Model
4.6.1. Traffic Model Per-Hop, Per-Flow Parameters
4.7. Per-hop Processing State
4.7.1. (per-hop, per-flow) Stateful: No
4.8. Algorithm parameters and mechanisms
4.9. Calculus
4.9.1. Published per-hop calculus: Yes
4.9.2. Published linear per-hop, per-flow calculus: Yes
4.9.3. Hop-by-hop jitter bounds: on-time
4.10. Packetization
4.10.1. Per-flow compatibility with per-hop source-routing: Yes
4.10.2. End-to-end packet header requirements
4.10.3. Hop-by-hop packet header requirements