## Slide 1: Problems with existing DetNet bounded latency queuing mechanisms draft-eckert-detnet-bounded-latency-problems-00
Toerless Eckert, Futurewei USA (tte@cs.fau.de)
Stewart Bryant, Stewart Bryant Ltd (sb@stewartbryant.com)
09/09/2021

## Slide 2: Summary
Various open issues in detnet related to queuing
High level:
Network / deployment
  Can we/how-can-we support popular network designs: SR-MPLS/SRv6 (and futre ones: BIER/BIER-TE)
  Can we/how-can-we support large-scale/wide-area networks with DetNet (MPLS WAN)
    Including preference for DiffServ, no controller-plane to P-LSR per-flow signaling
  How much can-we/should we have lower-cost DetNet options via no or reduced clock synchronization requirements ?
Application
  Bounded latency not always enough!
  Tightly bounded jitter can improve value of service
Slides highlighting only subset of issues, draf more comprehensive

## Slide 3: IntServ / TSN-ATS, DetNet model (issues)
(3)
Select
Prio Q
for k
(2)
Shape
to
k/ k
(1)
Look
Up
Flow k
PRIO1
PRIO2
PRIO8
…
1 msec
2 msec
8 msec
Max
delay
(4)
Strict tPrio Q
Per-flow state table
Per Hop Behavior
In Forwarding Plane
all on egress
Sender
e.g.
Flow k
IntServ/
TSN-ATS
Edge
IntServ/
TSN-ATS
Forwarder
IntServ/
TSN-ATS
Forwarder
IntServ/
TSN-ATS
Forwarder
Receiver
e.g.
Flow k
IntServ/
TSN-ATS
Forwarder
(1) Look up Flow k |  | Steer Flow | (2) Shaper param / state vars |  |  |  | (3)
L2 (TSN) or L3 (DetNet) Flow Key | Flow# k | Next Hop | k | k | time stamp | level | Queue
(S1,D1,Sport1, Dport1, Prot1) | 1 | … | … | … | … | … | 5
(S2,D2,Sport2, Dport2, Prot2) | 2 | … | … | … | … | … | 3
 | … | … |  |  |  |  | 
(S50k,D50k,Sport50k, Dport50k, Prot50k) | 50,000 | ... | … | … | … | … | 1
(1) Look up Flow k |  | Steer Flow | (2) Shaper param / state vars |  |  |  | (3)
L2 (TSN) or L3 (DetNet) Flow Key | Flow# k | Next Hop |  |  | time stamp | level | Queue
(S1,D1,Sport1, Dport1, Prot1) | 1 | … | … | … | … | … | 5
(S2,D2,Sport2, Dport2, Prot2) | 2 | … | … | … | … | … | 3
 | … | … |  |  |  |  | 
(S50k,D50k,Sport50k, Dport50k, Prot50k) | 50,000 | ... | … | … | … | … | 1
Flow k requirements
k/ k
End-to-end
Min..max latency
(Calculate path
or use shortest path
(slide does not show path steering)
Calculate best queue for each hop to meet min..max latency
<=>
Flow fits ?
Admit
else reject
Network resource Database
Per-link/hop, per-queue free space
link free bandwidth
Per-flow, per-hop Database
Flow k: k/ k , {Qi }
Install flow k params on every hops per-flow state table
ACK/
NAK
Flow
REQUEST
Controller
Ingres
PE
P
P
P
Egress
PE

## Slide 4: Desirable DetNet QoS option
Sender
e.g.
Flow k
Ede-Gate
DiffServ
Flow- stateless
DiffServ
Flow- stateless
DiffServ
Flow- stateless
Receiver
e.g.
Flow k
DiffServ
Flow- stateless
Flow k requirements
k/ k
End-to-end
Min..max latency
(Calculate path
or use shortest path
(slide does not show path steering)
Calculate best queue for each hop to meet min..max latency
<=>
Flow fits ?
Admit
else reject
Network resource Database
Per-link/hop, per-queue free space
link free bandwidth
Per-flow, per-hop Database
Flow k: k/ k , {Qi }
Install flow k params on every hops per-flow state table
ACK/
NAK
Flow
REQUEST
Controller
Ingres
PE
P
P
P
Egress
PE
DiffServ only, per-class QoS

## Slide 5: Per-Hop, Per-flow state issues
Core of IntServ (RFC2212), quickly amended by DiffServ. No DiffServ deployed significantly in networks larger than campus.
  Reduced IntServ, RSVP-Traffic-steering, NOT-per-hop-queuing was used until better technology was available (Segment Routing).
  This is more expensive the faster the network is.
Several issues with per-hop, per-flow state
  QoS hardware cost limitation: Shaper – IntServ -> Interleaved Regulators (UPS, TSN-ATS), still too expensive for large-scale, high-speed forwarders with many interfaces.
  Churn through signaling updates. Per-Hop, Per-Flow state upates upon chage: new/dead flows, path changes. Update to hardware.
  If state is driven by application, state on P nodes even more problematic (unplannable). Biggest experiences from IP multicast and evolution of IETF standards for that.
Current standard or proposed standard for large-scale network models: no per-hop, per-flow statee: Segment Routing (source routing), BIER(-TE) or multicast , simple DiffServ QoS
  Need DetNet QoS option supporting SR, BIER…

## Slide 6: Tightly bounded jitter – “In-time” vs. “On-time” (1)
Latency
0
“In-time”
path propagation latency
O(speed of light ,link serialization)
maximum path queuing jitter
min .. max queuing latency
Packets with no
Queuing latency
(zero congestion)
Packets with max
Queuing latency
(max congestion)
Latency
0
“On-time”
path propagation latency
O(speed of light ,link serialization)
Close to zero path queuing jitter
min .. max queuing latency
In-network, every hop
Packet buffering hiding jitter From receiver
Queuing jitter
For an packets
Any congestion
“In-time” delivers packets as soon as possible.
  Under no congestion, no in-network queuing latency incurred
  IETF IntServ/Guaranteed Service, TSN-ATS use this model
  Queuing latency only because of
    Temporary congestion / burst accumulation of packets from multiple interfaces arriving into same output queue
    Per-flow interleaved regulator / shaper – to remove bursts introduced by 1.
“In-time” creates worst-case jitter between no..max traffic load
On-time eliminates this jitter
  By networking buffering independ of traffic load

## Slide 7: Tightly bounded jitter – “In-time” vs. “On-time” (2)
Why/when in-time vs. on-time ?
Non-application reasons:
  Current on-time (e.g.: CQF) requires clock synchronization. In-time can work without any clock synchronization. If applications do not benefit from on-time (tight jitter), then in-time can be a simpler solution
  Curent in-time solutions (e.g.: TSN-AT IETF-GS) require per-hop, per-flow controller-plane instantiatd state – this can be a challenge (see prior slides). If applications do not benefit from in-time (lower latency under lower network load), then on-time can be the better solution.
The application view:
  All deterministic application MUST be prepared for any packet to arrive as late as (guaranteed) bounded latency
  Only SOME deterministic applications can be built to operate opportunistically better with in-time
    Network load low  lower latency/RTT  deterministic application may operate faster / more-accurate / “somewhat better”
    But there is no GUARANTEE for any of this – it is OPPORTUNISTIC! Network load can always change unexpectedly, burst collisions can happen stochastically !
  In-time often also shifts work from network into application/device !

## Slide 8: Tightly bounded jitter – “In-time” vs. “On-time” (3)
Actor
PLL
Phase Locked Loop
compute
Dejitter
Playout
Synchronize
Buffer
Application traffic profiles, e.g.: Industrial Internet Consortium (IIC) Time Sensitive Networks for Flexible Manufacturing Testbed https://www.iiconsortium.org/white-papers.htm
  Isochronous, Cyclic, Audio-Video, (on-time), Alarm and Events (in-time), …
Media playout and most control loops want on-time
  Media: Synchronous playout
  If network is in-time, packets must be buffered in application and consumed at maximum guaranteed latency time
Playout buffer size requirement depend on network jitter == network size
  Expensive war stories in industry when equipment was used in networks with higher jitter
In-time also raises clock synchronization needs on devices
  On-time delivered packets carry implicit timing information !
  Dumb devices (actors) may not be able to support dejittering and/or accurate clock
  Classical example: accurate PLC with periodic “polling” of dumb actors/sensor without accurate clock: on-time allows for isochronous operation.
    In-time would require much more complex sensor/actor/control-loops
Programmable
Logic Controller
Sensor
Network
latency
and jitter
compensation
Measurement
Packet
PLC
Command
Packet
Measurement
Packet
Command
Packet
Command
effect
Dejitter
Synchronize

## Slide 9
Comparison of TSN/DetNet options | IntServ/GS RFC2212 | TSN-ATS Latest (2020) TSN standard, also prime target for Detnet | TSN-CQF (Qcr) Original/simplified TSN option (over Qbv) | Packet taged CQF draft-dang-queuing-with-multiple-cyclic-buffers | Packet tagged per-hop deadlines draft-stein-srtsn
DiffServ / SR-MPLS,v6 / BIER design goal compatible | NO | NO | YES | YES | YES
Per-hop-per-flow state Hardware-cost/scale Signalling-complexit/churn | YES | YES Interleaved regulators (simplified over GS) | NO | NO | NO
Clock synchronization required Additional PTP hardware and network operational requirements | NO | NO | YES High accuracy (nsec) | YES Low accuracy (usec) | TBD ? Not considered to be a deployment cost by author ?!
Tighly bounded jitter | No | No | Yes Usec jitter (cycle size) | Yes Usec jiter (cycle size) | No ?
Target deployment scale | 1990th “Internet” | Building/ Campus? | Building/ Campus? | Campus/Metro/ Country (tested) | Metro ?
Arbitrary physical distance network / network links | YES | YES | NO Throughput deteriorating to 0 at ca. 2 km | YES | Yes ?
Latency calculus (for PCE) | Complex, deterministic | Simple, deterministic | Trivial, deterministic | Trivial, deterministic | TBD – ongoing work to be published

## Slide 10: Q & A