## Slide 1: Deterministic Networking (DetNet) Data Plane MPLS TC Tagging for Cyclic Queuing and Forwarding (MPLS-TC TCQF) draft-eckert-detnet-mpls-tc-tcqf-00
Toerless Eckert, Futurewei USA (tte@cs.fau.de)
Stewart Bryant, University of Surrey ICS (s.bryant@surrey.ac.uk)
09/09/2021

## Slide 2: Why ?
Bounded latency solution for DetNet …
Derived from IEEE TSN “Cyclic Queuing and Forwarding” (CQF 802.1Qch-2017)
  CQF Problem: assigns pakets to cyclic buffer by receive timestamp
    Limits range to few Km hops, then hop latency exceeds cycle time.
    Requires sub cycle-time accurate cock synchronization
Tagged CQF (TCQF)
  Solves CQF issues by carrying cycle identifier in packet header field
  Allows for more than 2 cycles
Benefits
  Simple/cos-effective queuing for high-speedlow-cost hardware, 100Gbps validated
  No per-hop, per-flow queuing state – no per-hop, per-queue controller plane interaction needed
    Scale, operational simplicity
    Can optionally support DiffServ model for DetNet (not required)
  No limitation for link propagation latency -> enables wide-area network DetNet services
  Simple controller plane calculus for admitting flows and calculating latency
    E.g.: Latency calculated in number of cycle times for each hop, admission based on bytes per cycle for a flow
  Tightly bounded jitter (cycle-time eg 100usec, 20usec,...)
    Can support all TSN traffic classes up to isochronous
    Bounded latency

## Slide 3: Tagged CQF with Multiple Buffers
Cycle Identifier (1..N, N = 2,3,..) in packet header
Receiving router preconfigured with cycle mapping table input to output cycle.
Packet put into output cycle buffer – and sent when its cycle is up.
More cycles allow for more variation in forwarding: MTIE and link propagation variation
cycle 1
cycle 2
cycle 3
cycle 1
cycle 2
cycle 3
cycle 1
cycle 2
cycle 1 buffer
sending
sending
cycle 3 buffer
sending
sending
sending
sending
cycle 2 buffer
Node 1 (sender)
Node 2 (“receiver”)
Outgoing interface
Link propagation latency

## Slide 4: Tagged CQF with Multiple Buffers
Cycle Identifier (1..N, N = 2,3,..) in packet header
Receiving router preconfigured with cycle mapping table input to output cycle.
Packet put into output cycle buffer – and sent when its cycle is up.
More cycles allow for more variation in forwarding: MTIE and link propagation variation
cycle 1
cycle 2
cycle 3
cycle 1
cycle 2
cycle 3
cycle 1
cycle 2
cycle 1 buffer
sending
sending
cycle 3 buffer
sending
sending
sending
sending
cycle 2 buffer
Node 1 (sender)
Node 2 (“receiver”)
Outgoing interface
cycle 1
cycle 2
cycle 3
cycle 4
cycle 3
cycle 4
cycle 1
cycle 1
cycle 1 buffer
sending
sending
cycle 3 buffer
sending
sending
sending
cycle 2 buffer
cycle 4 buffer
sending
Link propagation latency with variation,
e.g.: Clock drift (MTIE)
Node 1 (sender)
Link propagation latency
Node 2 (“receiver”)

## Slide 5: How
Multiple Buffer, Tagged CQF decription of operations, benefits:
  draft-qiang-detnet-large-scale-detnet (expired), draft-dang-queuing-with-multiple-cyclic-buffers
  Informational – do not specify actual forwarding plane specific encap/forwarding behavior.
This draft
  Proposed standards track TCQF spec for DetNet MPLS Data Plane
    Using Traffic Class (TC) of Top of Stack (ToS) MPLS Label Stack Entry (LSE)
  Complies with MPLS DiffServ [RFC3270] TC-inferred PSC LSP (E-LSP) behavior
    Occupies one TC value by cycle (e.g.: 4 TC for prior slide 4 cycle setup)

## Slide 6: Section 2/4: Using TCQF with DetNet MPLS
DetNet MPLS Relay Transit Relay DetNet MPLS
End System Node Node Node End System
T-PE1 S-PE1 LSR-P S-PE2 T-PE2
+----------+ +----------+
| Appl. |<------------ End-to-End Service ----------->| Appl. |
+----------+ +---------+ +---------+ +----------+
| Service |<--| Service |-- DetNet flow --| Service |-->| Service |
+----------+ +---------+ +----------+ +---------+ +----------+
|Forwarding| |Fwd| |Fwd| |Forwarding| |Fwd| |Fwd| |Forwarding|
+-------.--+ +-.-+ +-.-+ +----.---.-+ +-.-+ +-.-+ +---.------+
: Link : / ,-----. \ : Link : / ,-----. \
+........+ +-[ Sub- ]-+ +......+ +-[ Sub- ]-+
[Network] [Network]
`-----' `-----'
|<- LSP -->| |<-------- LSP -----------| |<--- LSP -->|
|<----------------- DetNet MPLS --------------------->|
Can run T-PE1 to T-PE2 – or on any subset (S-PE1 – S-PE2)
TBD: ingres function: shape DetNet flows into cyclic queuing (some known TSN gate functions or similar).
TCQF state not tied to DetNet flow state in forwarding plane on midpoints (but in controller plane for admission control)
  ToS LSE that holds TC with TCQF semantic can be Servic Label (S-Label) or Forwarding Label (F-Label) – up to controller plane
Draft discusses when DetNet service layer operation require to re-do ingres function
  Only Packet Reordering Function (PRF) – causes change in burstyness of flow packets.

## Slide 7: Section 3: Data model (and textual forwarding description)
module ietf-detnet-tcqf
augment TBD
+--rw tcqf-config
| +--rw cycles uint16
| +--rw cycle-time uint16
| +--rw cycle-clock-offset uint32
| +--rw tcqf-if-config* [oif-name]
| +--rw oif-name if:interface-ref
| +--rw cycle-clock-offset int32
| +--rw tcqf-iif-cycle-map* [iif-name]
| +--rw iif-name if:interface-ref
| +--rw iif-cycle-map* [iif-cycle]
| +--rw iif-cycle uint8
| +--rw oif-cycle uint8
|
+--rw tcqf-mpls-tc-tag* [name]
+--rw name if:interface-ref
+--rw cycle* [cycle]
+--rw cycle uint8
+--rw tc uint8
YANG data model to configure TCQF: domain-wide cycle-time, cycles, clock-offsets
Per TCQF Interface config: per-input-interface cycle-map table
Encapsulation dependent: per-interface cycle-ID to packet-tag mapping (here only MPLS-TC encap specified)

## Slide 8: Section 5: Data plane pseudocode (1) Receive … TCQF enqueue packet
tcqf = ietf-detnet-tcqf
void receive(pak) {
// Receive side TCQF - remember cycle in
// packet internal header
iif = pak.context.iif
if(tcqf.tcqf-if-config[iif]) { // TCQF enabled
if(tcqf.tcqf-mpls-tc-tag[iif]) { // TC-TCQF
pak.context.tcqf_cycle =
map_tc2cycle(pak.mpls_header.lse[tos].tc,
tcqf.tcqf-mpls-tc-tag[iif])
} else // future encap/tagging options for TCQF
}
// Forwarding including any label stack operations
oif = pak.context.oif = forward_process(pak)
// ... optional DetNet PREOF functions here
// ... if router is DetNet service node
// Output interface TCQF enqueuing
if(pak.context.tcqf_cycle && // non TCQF packets value is 0
tcqf.tcqf-if-config[oif]) { // TCQF enabled
// Map tcqf_cycle for iif to oif mapping table
cycle = pak.context.tcqf_cycle = map_cycle(cycle,
tcqf.tcqf-if-config[oif].tcqf-iif-cycle-map[[iif])
// Map cycle to TC value of ToS LSE
if(tcqf.tcqf-mpls-tc-tag[iif]) { // TC-TCQF
pak.mpls_header.lse[tos].tc =
map_cycle2tc(cycle, tcqf.tcqf-mpls-tc-tag[oif])
} else // future encap/tagging options for TCQF
// Enqueue into cycle buffer
tcqf_enqueue(pak, oif.cycleq[cycle])

## Slide 9: Section 5: Data plane pseudocode (2) TCQF packet sending
// Started when TCQF is enabled on an interface
void send_tcqf(oif) {
// Calculate correct time to start sending cycle 1
cycle = 1
cc = tcqf.tcqf-config.cycle-time *
tcqf.tcqf-config.cycle-time
o = tcqf.tcqf-config.cycle-clock-offset
nextcyclestart = floor(tnow / cc) * cc + cc + o
// Send cycles forever
while(1) {
while(tnow < nextcyclestart) { } // Wait until next cycle starts
while(pak = dequeue(oif.cycleq(cycle)) {
send(pak)
}
cycle = (cycle + 1) mod tcqf.tcqf-config.cycles + 1
nextcyclestart += tcqf.tcqf-config.cycle-time
}
}

## Slide 10: More
Details in doc, not explained in slides:
  Example controller plane math to calculate cycle mapping
Missing / TBD ?!
  Ingres function, shapping into cycles
    Do we need this in TCQF specific ? TSN Gates would work.
    We would likely want/need those for other DetNet QoS options too ?
    E.g.: TBD what to do
  Complete YANG model specification
    Just writing exercise
  What else ?

## Slide 11: Q & A