## Slide 1
Proposed evaluation template For draft-ietf-detnet-scaling-requirements-03
NOT (YET) APPROVED BY ANYONE EXCEPT THE AUTEHOR
Toerless Eckert, Futurewei USA (tte@cs.fau.de)
V0.0, 09/07/2023

## Slide 2: What is being evaluated
Mechanisms that support bounded latency across a DetNet domain
This document proposes for requirements to be distinguised to where they apply:
  “P”: P router / Hop-by-hop processing
  “PE”: ingress PE router processing

## Slide 3: PE functions
On ingress to a DetNet domain, all flows need to be processed on a per-flow basis because received traffic flows need to be policed to comply with their admitted traffic envelope.
  Complexity / scalability on PE node can therefore never be as high as on P node.
  Note: in simple ring topologies, every node is a P and PE node. If a ring has 20 nodes, then a node will typically be PE for only 1/20’th of the overall flows. So P scalability is even important in these topologies. Larger ring topologies will have ring nodes that are hubs for a larger number of spokes, and hence ring nodes are only P nodes.
Hop-by-hop forwarding mechanism may need specific ingress PE processing beyond policing. This needs to be evaluated.
  Example: cycle mechanisms need per-flow timing of admitting packets of a flow into specific cycles. This is a specific version of a generic policer.
draft-eckert-detnet-flow-interleaving makes the argument that policing and timing of flows on ingress PE is a generic function that DetNet is currently missing, but which if defined could be combined with all hop-by-hop mechanisms and act as the common additional PE function
  This would be a simplified version of the TSN timed gates function (which in TSN is allowed to be used on every hop, but in “scaling” DetNet only on ingress PE
In current sheet, only one requirement is identified as “only applicable to PE”. Other requirements have not been identified to have specific different requirements for PE, so only P is indicated.

## Slide 4: Enhancements to evaluation sheet
New column to indicate whether requirement is per-hop (P), or ingress (PE).
Split 3.1 into its four constituent requirements (3.1.1 - 3.1.4)
  No evaluation for 3.1 overall, just the four individual ones
  No evaluation for 3.1.4, because synchronous hop-by-hop such as *CQF can also provide support for asynchronous flows, for example by burs shaping as a domain ingress function. Has benefits over per-hop burst shaping as in rfc2211 or multi-priority burst-shaping as in Qcr/gLBF. Need to revisit requirement.
3.2.1 Added requirement for single-hop transmission jitter (NEW)
3.8(1) List explicit requirement for “support tight jitter (per-hop)”
  as mentioned in requirements document as one possible option of traffic (e.g.: industrial control loops)

## Slide 5: <Mechanism> evaluation (<notes>)
Sec. | P/PE | Requirements | Eval | Notes |  |  | 
3.1.1 | PE | Async across TSN subdomains |  | changes from overall section 3 eval to individuals |  |  | 
3.1.2 | P | Tolerate Clock Jitter/Wander |  |  |  |  | 
3.1.3 | P | No Full Time Sync required |  |  |  |  | 
3.2 | P | Large Single-hop Propagation Latency |  |  |  |  | 
3.2.1 | P | Support single-hop propagation jitter |  | New |  |  | 
3.3 | P | Support Higher Link Speed |  |  |  |  | 
3.4(1) | P | Scalable to Large Number of Flows |  | Details from prior reviews |  |  | 
3.4(2) | P | Tolerate High Utilization |  | Details from prior reviews |  |  | 
3.5 | P | Link/Node failures, Topo Changes |  |  |  |  | 
3.6 | P | Prevent Flow Fluctuation from Disrupting Service |  |  |  |  | 
3.7 | P | Scalable to Large Number of Hops with Complex Topology |  |  |  |  | 
3.8(1) | P | Support tight jitter/sync-control loops |  | New |  |  | 

## Slide 6: Possible evaluation points
3.1.1 YES if hop-by-hop mechanism has defined ingress function, and/or assumed to be combined with some pre-existing ingress function. Describe or reference to ingress function in notes.
3.1.2 Suggest YES if permitted drift (short term variation of clock frequency) on a 100Gbps (or faster) link can be equal or less than 1 usec.
3.1.3 YES if MTIE (maximum time interval error) over arbitrary periods can be infinite. Or (simpler): if clock wander over 24 hours can be larger than 100ppm ~= 8 seconds.
3.1.4 Not evaluated, see prior discussion why.
3.2 YES if 1000km links can be supported (on every hop)
3.1.2 NEW: YES if jitter in link latency can be supported (length variation, L2 retransmission jitter on mobile/radio links,...)
3.3 YES if 100Gbps or faster links can be supported without loss of performance (e.g.: higher dead times) than for slower links.
3.4(1) YES if mechanism does not require per-hop, per-flow state requiring per-packet lookup and read/write cycles.
3.4(2) YES if 100Gbps or faster long latency links permit same close to 100% DetNet traffic
3.5 YES if Segment Routing and fast-reroute options with resource reservation can be supported
3.6 YES if mechanism does not have burst-accumulation across multiple network hops (no per-hop increase in flow burstyness) AND if mechanism allows to add/delete flows without impacting prior latency/jitter guarantees of pre-existing flows
3.7 YES if 3.6 is YES AND if flow interleaving can be applied to the mechanism across flows from different ingress/egress PE
3.8(1) YES if end-to-end jitter is independent of number of hops.

## Slide 7: Example: TCQF/CQSF evaluation (comparison to CQF/ECQF/glBF highlighted)
Sec. | P/PE | Requirements | Eval | Notes |  |  | 
3.1.1 | PE | Async across TSN subdomains | Yes | TCQF defines async ingres function. |  |  | 
3.1.2 | P | Tolerate Clock Jitter/Wander | Yes | E.g.: with 4 cycles, max jitter/wander 1 cycle time. Main benefit over (E)CQF ECQF can not do this: arrival time inaccuracy leads to wrong cycle assumption |  |  | 
3.1.3 | P | No Full Time Sync required | No/ “NA” | Same as CQF, ECQF, TAS. Main benefit of gLBF (which has YES) Lower accuracy clock sync requirements than CQF/ECQF |  |  | 
3.2 | P | Large Single-hop Propagation Latency | Yes | Main benefit over TAS, CQF. Same as ECQF. |  |  | 
3.2.1 | P | NEW: Support single-hop propagation jitter | Yes | Benefit over ECQF , CQF, TAS (radio, retransmissions, length deviation) |  |  | 
3.3 | P | Support Higher Link Speed | Yes | 200km/100Gbps proven, can scale well beyond that. Not proven for ECQF |  |  | 
3.4(1) | P | Scalable to Large Number of Flows | Yes | No per-hop, per-flow state, read/write memory access requirement |  |  | 
3.4(2) | P | Tolerate High Utilization | Yes | Solves CQF issue, equal/better than ECQF: No dead times. |  |  | 
3.5 | P | Link/Node failures, Topo Changes | NA? / Yes | CSQF: Could support all Segment Routing re-route soutions (path, tunnel,...) |  |  | 
3.6 | P | Prevent Flow Fluctuation from Disrupting Service | Yes | Like CQF/ECQF: No burst accumulation/jitter-increase due to per-hop cycle based reshapeper-hop reshaping. |  |  | 
3.7 | P | Scalable to Large Number of Hops with Complex Topology | Good (TCQF) Best (CSQF) | Assuming flow interleaving on edge, like CQF/ECQF CSQF more flexible than TSQF, CQF/ECQF |  |  | 
3.8(1) | P | Support tight jitter/sync-control loops | Yes | Network size independent hop-by-hop/end-to-end jittter ~ O(0) |  |  |