## Slide 1
Proposed improved template
2. Evaluations TCQF / CSQF: draft-eckert-detnet-tcqf ,draft-chen-detnet-sr-based-bounded-latency
gLBF: draft-eckert-detnet-glbf
3. Revisited ECQF evaluation (Appendix)
Toerless Eckert, Futurewei USA (tte@cs.fau.de) (slide editor)
for the authors of above drafts
IETF DETNET Interim, 09/2023 rev 1.0 9/11/2023

## Slide 2: Proposed improved Template
And why

## Slide 3: Enhancements to evaluation sheet
New column to indicate whether requirement is per-hop (P), or ingress (PE).
Split 3.1 into its four constituent requirements (3.1.1 - 3.1.4)
  No evaluation for 3.1 overall, just the four individual ones
Modified 3.1.4 to “Support aperiodic flows” – indicate whether on P or PE
  Requirement for no-clock-sync already covered by 3.1.3
  Requirement draft implies this is only possible with per-hop asynchronous mechanisms. This is not true.
  E.g.: TCQF/CSQF can support aperiodic flows via ingress-PE flow-interleaving (adds latency on PE hop)
    E.g.: Delay on ingress by up to 500 usec to keep small per-hop (cycle) latency on all following hops (spread bursts over 500 usec)
  Asynchronous per-hop (P) method (rfc2211/Qcr/gLBF) come at the price of increased per-hop guaranteed latency which adds up across long paths! – See draft-eckert-detnet-flow-interleaving
3.2.1 Added evaluation for single-hop propagation jitter (NEW)
  Because of: RAW (reflections, interference, retransmission), length deviation (wired)
3.8(1) List explicit evaluation for “support tight jitter (per-hop)”
  as mentioned in requirements document as one possible option of traffic (e.g.: industrial control loops)

## Slide 4: <Mechanism> evaluation (<notes>)
Sec. | P/PE | Requirements | Eval | Notes |  |  | 
3.1.1 | P/PE | Async across TSN subdomains |  | changes from overall section 3 eval to individuals |  |  | 
3.1.2 | P | Tolerate Clock Jitter/Wander |  |  |  |  | 
3.1.3 | P | No Full Time Sync required |  |  |  |  | 
3.1.4 | P/PE | Support for aperiodic flows |  |  |  |  | 
3.2 | P | Large Single-hop Propagation Latency |  |  |  |  | 
3.2.1 | P | Support single-hop propagation jitter |  | New |  |  | 
3.3 | P | Support Higher Link Speed |  |  |  |  | 
3.4(1) | P | Scalable to Large Number of Flows |  | Details from prior reviews |  |  | 
3.4(2) | P | Tolerate High Utilization |  | Details from prior reviews |  |  | 
3.5 | P | Link/Node failures, Topo Changes |  |  |  |  | 
3.6 | P | Prevent Flow Fluctuation from Disrupting Service |  |  |  |  | 
3.7 | P | Scalable to Large Number of Hops with Complex Topology |  |  |  |  | 
3.8(1) | P | Support tight jitter/sync-control loops |  | New |  |  | 

## Slide 5: Evaluations used / suggested
3.1.1 YES if hop-by-hop mechanism has defined ingress function, and/or assumed to be combined with some pre-existing ingress function. Describe or reference to ingress function in notes.
3.1.2 Suggest YES if permitted drift (short term variation of clock frequency) on a 100Gbps (or faster) link can be as large as 1 usec (e.g.: no as tight as 100 nsec or less).
3.1.3 YES if MTIE (maximum time interval error) over arbitrary periods can be infinite. Or (simpler): if clock wander over 24 hours can be larger than 100ppm ~= 8 seconds.Partial: clock sync requirements are proven to work for large-scale networks
3.1.4 Indicate whether support for aperiodic flows happens per-hop (P) or on PE.
3.2 YES if 1000km links can be supported (on every hop)
3.1.2 NEW: YES if jitter in link latency can be supported (length variation, L2 retransmission jitter on mobile/radio links,...)
3.3 YES if 100Gbps or faster links can be supported without loss of performance (e.g.: higher dead times) than for slower links.
3.4(1) YES if mechanism does not require per-hop, per-flow state requiring per-packet lookup and read/write cycles.
3.4(2) YES if 100Gbps or faster long latency links permit same close to 100% DetNet traffic
3.5 YES if Segment Routing and fast-reroute options with resource reservation can be supported
3.6 YES if mechanism does not have burst-accumulation across multiple network hops (no per-hop increase in flow burstyness) AND if mechanism allows to add/delete flows without impacting prior latency/jitter guarantees of pre-existing flows
3.7 YES if 3.6 is YES AND if flow interleaving can be applied to the mechanism across flows from different ingress/egress PE
3.8(1) YES if end-to-end jitter is independent of number of hops.

## Slide 6: Justification: PE functions
On ingress to a DetNet domain, all flows need to be processed on a per-flow basis because received traffic flows need to be policed to comply with their admitted traffic envelope.
  Complexity / scalability on PE node can therefore never be as high as on P node.
  Note: in simple ring topologies, every node is a P and PE node. If a ring has 20 nodes, then a node will typically be PE for only 1/20’th of the overall flows. So P scalability is even important in these topologies. Larger ring topologies will have ring nodes that are hubs for a larger number of spokes, and hence ring nodes are only P nodes.
Hop-by-hop forwarding mechanism may need specific ingress PE processing beyond policing. This needs to be evaluated.
  Example: cycle mechanisms need per-flow timing of admitting packets of a flow into specific cycles. This is a specific version of a generic policer.
draft-eckert-detnet-flow-interleaving makes the argument that policing and timing of flows on ingress PE is a generic function that DetNet is currently missing, but which if defined could be combined with all hop-by-hop mechanisms and act as the common additional PE function
  This would be a simplified version of the TSN timed gates function (which in TSN is allowed to be used on every hop, but in “scaling” DetNet only on ingress PE
In current sheet, only one requirement is identified as “only applicable to PE”. Other requirements have not been identified to have specific different requirements for PE, so only P is indicated.

## Slide 7: TCQF / CSQF evaluation

## Slide 8: Common evaluation because:
Same common per-hop logic
  Same ingress processing (PE)
  N-cycle forwarding hop-by-hop
    E.g.: any TSN switch could do it, 100Gbps low-cost validation exist
  Packet is assigned to cycle by a packet header field.
Difference
  TCQF: packet header field is single cycle-field, rewritten on every hop
    Allows to use IP-DSCP, MPLS-TC – and thus work in IP/IPv6 and MPLS networks – without SR.
    Can also be combined with SR (orthogonal)
  CSQF: cycle derived on every hop from Segment Routing header
    N SIDs per hop to indicate N different cycles
    IPv6: SRH, future compressed SRH, SR-MPLS
We think: Any implementation that can do TCQF and supports SR can also do CSQF
Differences relevant to evaluation only in one point

## Slide 9: TCQF & CSQF evaluation
Sec. | P/PE | Requirements | Evaluation | Notes |  |  | 
3.1.1 | PE | Async across TSN subdomains | Yes | TCQF defines async ingres. Same applicable to CSQF |  |  | 
3.1.2 | P | Tolerate Clock Jitter/Wander | Yes | E.g.: with 4 cycles, max jitter/wander 1 cycle time. Main benefit over (E)CQF ECQF can not do this: arrival time inaccuracy leads to wrong cycle assumption |  |  | 
3.1.3 | P | No Full Time Sync required | partial | Same as CQF, ECQF, TAS. Main benefit of gLBF (which has YES) Partial: ca. 90% lower accuracy clock sync req. than with CQF/ECQF |  |  | 
3.1.4 | PE | Support for aperiodic flows | Yes | Via aperiodic burst shape/delay on ingress PE or overprovisioning. |  |  | 
3.2 | P | Large Single-hop Propagation Latency | Yes | Main benefit over TAS, CQF. Same as ECQF. |  |  | 
3.2.1 | P | Support single-hop propagation jitter | Yes | Benefit over ECQF , CQF, TAS (radio, retransmissions, length deviation) |  |  | 
3.3 | P | Support Higher Link Speed | Yes | 200km/100Gbps proven, can scale well beyond that. Not proven for ECQF |  |  | 
3.4(1) | P | Scalable to Large Number of Flows | Yes | No per-hop, per-flow state, read/write memory access requirement |  |  | 
3.4(2) | P | Tolerate High Utilization | Yes | Solves CQF issue, equal/better than ECQF: No dead times |  |  | 
3.5 | P | Link/Node failures, Topo Changes | Yes | Can support Segment Routing and hence all re-route, path-fixing options (TCQF, CSQF). CSQF: even defined solely for SR! |  |  | 
3.6 | P | Prevent Flow Fluctuation from Disrupting Service | Yes | Like CQF/ECQF: No burst accumulation/jitter-increase due to per-hop cycle based reshapeper-hop reshaping. |  |  | 
3.7 | P | Be Scalable to a Large Number of Hops with Complex Topology | Good (TCQF) Best (CSQF) | Assuming flow interleaving on edge, like CQF/ECQF CSQF more flexible than TSQF, CQF/ECQF |  |  | 
3.8(1) | P | Support tight jitter/sync-control loops | Yes | Network size independent hop-by-hop/end-to-end jittter ~ O(0) |  |  | 

## Slide 10: Comparison CQF / ECQF / TCQF & CSQF - “Yes” – with other TSN means
Sec. | P/PE | Requirements | CQF | ECQF | TCQF/CSQF | Notes |  |  | 
3.1.1 | PE | Async across TSN subdomains | “Yes” | “Yes” | Yes | TCQF defines async ingres. Same applicable to CSQF |  |  | 
3.1.2 | P | Tolerate Clock Jitter/Wander | No | No | Yes | E.g.: with 4 cycles, max jitter/wander 1 cycle time. Main benefit over (E)CQF ECQF can not do this: arrival time inaccuracy leads to wrong cycle assumption |  |  | 
3.1.3 | P | No Full Time Sync required | No | No | partial | Same as CQF, ECQF, TAS. Main benefit of gLBF (which has YES) Partial: ca. 90% lower accuracy clock sync req. than with CQF/ECQF |  |  | 
3.1.4 | PE | Support for aperiodic flows | “Yes” | “Yes” | Yes | Via aperiodic burst shape/delay on ingress PE or overprovisioning. |  |  | 
3.2 | P | Large Single-hop Propagation Latency | No | Yes | Yes | Main benefit over TAS, CQF. Same as ECQF. |  |  | 
3.2.1 | P | Support single-hop propagation jitter | No | No | Yes | Benefit over ECQF , CQF, TAS (radio, retransmissions, length deviation) |  |  | 
3.3 | P | Support Higher Link Speed | partial | partial | Yes | 200km/100Gbps proven, can scale well beyond that. Not proven for ECQF |  |  | 
3.4(1) | P | Scalable to Large Number of Flows | partial | partial | Yes | No per-hop, per-flow state, read/write memory access requirement |  |  | 
3.4(2) | P | Tolerate High Utilization | No | Yes | Yes | Solves CQF issue, equal/better than ECQF: No dead times |  |  | 
3.5 | P | Link/Node failures, Topo Changes | No (TSN) | No (TSN) | Yes | Can support Segment Routing and hence all re-route, path-fixing options (TCQF, CSQF). CSQF: even defined solely for SR! |  |  | 
3.6 | P | Prevent Flow Fluctuation from Disrupting Service | Yes | Yes | Yes | Like CQF/ECQF: No burst accumulation/jitter-increase due to per-hop cycle based reshapeper-hop reshaping. |  |  | 
3.7 | P | Be Scalable to a Large Number of Hops with Complex Topology | No (TSN) | No (TSN) | Good (TCQF) Best (CSQF) | Assuming flow interleaving on edge, like CQF/ECQF CSQF more flexible than TSQF, CQF/ECQF |  |  | 
3.8(1) | P | Support tight jitter/sync-control loops | Yes | Yes | Yes | Network size independent hop-by-hop/end-to-end jittter ~ O(0) |  |  | 

## Slide 11: 3.4 explanations
No per-hop, per-flow state in routers
  No need for per-packet “single-cycle” read, calculate, write processing of router flow-state memory as in e.g.: TSN-ATS interleaved regulators.
Large scale simulation result in 2020 published IEEE research paper
100Gbps low-cost FPGA router based, 2000km long network path validation in China
  Includes feasibility of network wide clock sync, e.g.: invalidates req. 3.1.3 in the context of PTP as required for TCQF/CSQF
Minimum HW complexity, number of queues / buffers required.
Reduced accuracy of clock synchronization / cycle timing vs. CQF / ECQF
  Low per-packet clock accuracy across complex, large router
  Because cycle number is in packet header, sender to receiver can have clock jitter / wander.

## Slide 12: 3.7 Explanations / justifications
Per-hop cycles avoid burst-accumulation (3.6). Strict per-hop latency.
Controller-plane manages per-flow resources per-hop.
  No per-hop forwarding plane config/state impact when flows are added/removed / re-routing
Addl. Improvement: Allocation of per-hop, per-cycle resources by controller-plane as for example explained in draft-eckert-detnet-flow-interleaving
  Timed gates on ingress PE router, no other forwarding plane impact.
  Examples shows path-length linear compute cost when allocating new flows, up to high utilization
Same logic applies to all of TCQF/CSQF, CQF/ECQF
  CSQF more flexible here than TCQF, CQF/ECQF – because it can define cycles per-hop in the packet header
    SR header as proposed, compressed SR header (SPRING) or DetNet header (e.g.: 4-bit/hop should be enough).
  Degree of improvement (higher utilization) for CSQF over TCQF ... 20% ?
  3.5: SR resilience options may be biggest benefit of CSQF over TCQF.

## Slide 13: gLBF evaluation

## Slide 14: gLBF evaluation (vs. CQF/ECQF/gLBF highlighted)
Sec. | P/PE | Requirements | Evaluation | Notes |  |  | 
3.1.1 | PE | Async across TSN subdomains | Yes | Naturally async, no special ingress function needed |  |  | 
3.1.2 | P | Tolerate Clock Jitter/Wander | Yes | Max per-hop jitter/wander just needs to be known/over-estimated during config |  |  | 
3.1.3 | P | Tolerate Time Asynchrony | Yes | Main benefit over CQF / ECQF / TCQF / CSQF |  |  | 
3.1.4 | P/PE | Support for aperiodic flows | Yes | Directly via P, or via additional ingress PE timed gates to increase utilization at lower end-to-end latency |  |  | 
3.2 | P | Large Single-hop Propagation Latency | Yes | Max hop propagation latency to be known/over-estimated during net. config. |  |  | 
3.2.1 | P | Support single-hop propagation jitter | Yes | Requires clock sync only across jittery link – not other links |  |  | 
3.3 | P | Support Higher Link Speed | TBD | Not yet proven in high-speed ASIC implementation. Target timed FIFO implementation model suggested for next-gen high-speed, low-cost.Impl. |  |  | 
3.4(1) | P | Scalable to Large Number of Flows | Yes | No per-hop, per-flow state, read/write memory access requirement |  |  | 
3.4(2) | P | Tolerate High Utilization | Yes | No dead times |  |  | 
3.5 | P | Link/Node failures, Topo Changes | Yes | Can support all Segment Routing re-route/path-control options. |  |  | 
3.6 | P | Prevent Flow Fluctuation from Disrupting Service | Yes | No burst accumulation/jitter-increase due to per-hop latency based re-shaping. |  |  | 
3.7 | P | Be Scalable to a Large Number of Hops with Complex Topology | Yes/TBD | Flow interleaving TBD |  |  | 
3.8(1) | P | Support tight jitter/sync-control loops | Yes | Network size independent hop-by-hop/end-to-end jittter ~ O(0) |  |  | 

## Slide 15: Explanations
3.4
  No per-hop, per-flow state in routers
  No per-hop, per-flow state in routers
    No need for per-packet “single-cycle” read, calculate, write processing of router flow-state memory as in e.g.: TSN-ATS interleaved regulators.
3.7
  TSN-ATS per-hop latency and calculus, but without per-hop/flow shaper (3.4)
    Damper mechanism to prohibit burst accumulation, replaces shapers.
    No control-plane to-per-hop signaling required.
    Flow changes only impact controller-plane, ingres-edge-router
  Applicability of flow interleaving for high utilization under review

## Slide 16: ECQF Eval revisited

## Slide 17: CQF / ECQF eval revisited
These slides only for comparison during discussion
ECQF 3.1 evaluation wrong. Was Yes, should be No:
  Definition Asynchrony: drift (MTIE) proportional to time, synchronous: drift (MTIE) has upper bound across arbitrary periods.
  Assume N (2,3,4) cycles: when clock drift exceeds N-cycle time, cycle mechanism will fail.
Note on 3.3 evaluation:
  10Gbps (fastest known CQF) -> 400 Gbps: 40x more accurate clock synchronization needed (impossible) to keep same percentage dead time. This improvement in accuracy is impossible.
  Therefore, dead time for 100G needs to be 10x higher than for 10G, and 40x higher than for 400G. Equally applies to ECQF.
  When packet arrives, arrival time determines assumed sending time. If sending time is within margin of accuracy, receiver time may be in the wrong cycle!

## Slide 18: CQF evaluation
sectionc | Requirements | Evaluation | Notes
3.1 | Tolerate Time Asynchrony | No | Rely on nanosecond clock synchronization across the entire network, where all network nodes align their cycle boundaries.
3.2 | Support Large Single-hop Propagation Latency | No | Link delay must be much smaller than cycle duration and considered negligible, so 2-buffer mode can work. Otherwise, 3-buffer (or more) mode is needed.
3.3 | Accommodate the Higher Link Speed | Partial | More buffer space is required for a specific length of cycle duration. Smaller cycle size may be chosen, but with a much smaller available zone.
3.4(1) | Be Scalable to the Large Number of Flows | Partial | Transmission gates are associated with each aggregated queue, but the stream filtering and policing actions per stream should be maintained.
3.4(2) | Tolerate High Utilization | No | The cycle duration includes a time zone called dead time (DT) contributed by Output delay, Link delay, Frame preemption delay, Processing delay, which can not be used to send packets.
3.5 | Prevent Flow Fluctuation from Disrupting Service | Partial | Requires corresponding flows setup algorithms to allocate resources appropriately among multiple flows to avoid transmission conflicts.
3.6 | Tolerate Failures of Links or Nodes and Topology Changes |  | Not related to queuing mechanisms directly.
3.7 | Be Scalable to a Large Number of Hops with Complex Topology | Partial/No (No from first eval) | It is more difficult to select the cycle time. Need making trade-offs between end-to-end delay and cycle duration.
3.8 | Support Multi-Mechanisms in Single Domain and Multi-Domains |  | Not related to a single queuing mechanism directly.
CQF (Cyclic Queuing and Forwarding), refer to IEEE 802.1Qch

## Slide 19: ECQF evaluation
section | Requirements | Evaluation | Notes
3.1 | Tolerate Time Asynchrony | Yes NO | Does not rely on time synchronization. Time-based CQF need frequency lock (frequency synchronization too). Count-based CQF can be more relaxed.
3.2 | Support Large Single-hop Propagation Latency | Yes | The cycle phase difference between two nodes is allowed. CPAP detect message covers link propagation delay.
3.3 | Accommodate the Higher Link Speed | Partial | More buffer space is required for a specific length of cycle duration. Smaller cycle size may be choosen, but with a much smaller available zone.
3.4(1) | Be Scalable to the Large Number of Flows | Partial | Transmission gates are associated with each aggregated queue, but the stream filtering and policing actions per stream should be maintained. Count-based bin need maintain state machine per flow.
3.4(2) | Tolerate High Utilization | No | Cyle size is always far less than burst interval, so overprovision (caused by burst / cycle) may cause low utilization. NOTE: based on the bandwidth reservation method in the document.
3.5 | Prevent Flow Fluctuation from Disrupting Service | Partial | Time-based CQF: may ensure CQF flows to be protected. Count-based CQF: may discard excess data above the contracted amount.
3.6 | Tolerate Failures of Links or Nodes and Topology Changes |  | Not related to queuing mechanisms directly.
3.7 | Be Scalable to a Large Number of Hops with Complex Topology | Partial | It is more difficult to select the cycle time. Need making trade-offs between end-to-end delay and cycle duration.
3.8 | Support Multi-Mechanisms in Single Domain and Multi-Domains |  | Not related to a single queuing mechanism directly.
ECQF (Enhancements to CQF), refer to IEEE 802.1Qdv