## Slide 1
Deterministic Networking (DetNet) Data Plane
Flow interleaving for scaling detnet data planes with minimal end-to-end latency and large number of flows draft-eckert-detnet-flow-interleaving-01
Toerless Eckert, Futurewei Technologies USA (tte@cs.fau.de),
IETF 117 DetNet WG meeting , rev 0.1
https://github.com/toerless/detnet/tree/main/slides

## Slide 2: Draft Goal / Summary
TSN has “Gates” to exactly time packets from flow
  Flexible tool for different purposes.
  Used hop-by-hop to build CQF
  Used on ingress and even hop-by-hop for “flow-interleaving”
  Other uses ?
DetNet Architecture should have Gates for Flow Interleaving
  I do not think we included them yet into our architecture
  Should be necessaryonly as ingress/edge function into DetNet domain (“PE function” only)
  Could leverage existing TSN HW capabilities where i=they exist.
    But difficult to adopt/deploy if we just hope a mix of DetNet and TSN Gates thrown in will work.
    Explicitly defining our spec needed (IMHO)
  Could be simplified if needed for scale (TBD details)
This draft just meant to be making that argument. Not the specification (yet)

## Slide 3: Why / Use-cases
Maximize possible DetNet utilization while maintaining minimal end-to-end queuing latency
  Benefits proportional to number of hops
  Benefits higher with lower link speeds
Does work best in with on-time per-hop queuing mechanisms
  Example: draft-eckert-detnet-tcqf (TCQF) draft-chen-detnet-sr-based-bounded-latency (CSQF)
  Text was actually split out from text to compare TCQF, SCQF
  Note: On-time queuing does not depend on this any more than in-time queuing does. But on-time can benefit from it more!

## Slide 4: Example use-case
Metro-Ring, e.g.: 30 hops (Bay-Area: 400 miles = 3 msec RTT light speed)
TCQF 20 usec cycle time: 15 * 20 * 1.5 (cycle) = 0.45 msec max one way queuing latency. Great low queuing latency re. distance RTT.
100 Gbps links = 166 * 1500 byte packet/cycle
Assume video based remote control applications
  50 FPS video, remote driving, video based machine control
  Assume each flow 1 * 1500 byte packet / frame (20 msec) (simplified)
Aka: many very low bitrate flows:
  Each flow only needs a 1500 byte packet in one out of 1000 cycles.
We can aggregate flows from any ingress Ri to egress R23, but that aggregation already requires to use gates to schedule each individual flow to be aggregated.
Single server: 100 (clients) * 30 (ring routers) = 3000 flows (just one example app).
  Still only 1.8 Gbps total – no bandwidth problem. Just low-latency management issue!
R30
R1
R16
R15
R7
R8
R24
R23
T1
T100
...
Server
Edge-Cloud
E.g.: radio towers

## Slide 5: Flow Interleaving
Solution: DetNet Controller Plane performs admission across e.g.: 100 msec worth of 20usec cycles (e.g.: 5000 cycles).
  Each flow out of potentially tenths of thousands of flows (with low bitrates) get admitted to a set of periodic cycles, e.g.: 20 msec apart. Flows are “distributed” across that time scale
  Not that difficult. Draft has example algorithm to do such “cycle-admission-control”. O(path-length)*O(#cycles/period) complexity.
  Complexity of finding optimized paths in complex topologies much higher. And that is done today in every large SP network.
Gates on ingress router is enforcing that packets for a flow are only released into DetNet domain at the right cycle(s)
R30
R1
R16
R15
R7
R8
R24
R23
T1
T100
...
Server
Edge-Cloud
E.g.: radio towers

## Slide 6: This is just a problem using cycles !
Let’s compare *QF (CQF, TCQF, CSQF), with TSN-ATS:
In TSN-ATS, per-hop guaranteed queuing latency is the sum of the burst size of flows
To guarantee e.g.: 20 usec per-hop queuing latency, TSN-ATS could also only admit 166 flows with a burst-size of 1500 bytes
Same problem of: how do we break through the 166 barrier
But not the same good solutions to it as we have with *QF
TSN-ATS is “in-time”: Jitter adds up: 20 usec/hop - compared to 20 usec end-to-end with *QF:
  Can not manage network capacity/latency in 20usec increments
  Maybe manage latency in worst-case intervals: 30 (hops) * 20 usec = 600 usec “virtual cycles”.
  Aka: 30 times less possible utilization. The one example application 1.8 Gbps could barely be made to fit 100 Gbps.
On-time mechanisms can really only increase per-hop burst-size/latency to manage utilization.
  Aggregation of multiple flows from same ingress to same egress no affected (gates can perfectly be used for that).

## Slide 7: TCQF vs CSQF
With TCQF, the cycle on every hop along the path is pre-determine by the initial cycle in which it is sent into the TCQF domain
When doing frame interleaving, some cycles along the path may be filling up faster than other... And may not be possible to avoid
  Example: application with 50 fps and 60 fps have cycle interference
With CSQF it is possible to spread out traffic across adjacent cycles easily and avoid these “overloaded cycles”
How important is this CSQF benefit ?
  Needs probably more complex real-world example than i have done so far
  But good to know that we easily have this option.

## Slide 8: Summary
We should include Gates into DetNet architecture
They help with flow-interleaving to increase utilization at low latency in DetNet.
With any per-hop queuing mechanism for flows from same ingress to same egress
B) When using on-time per-hop queuing mechanism (*QF), they permit even higher utilization by allowing interleaving between flows from different ingress to different egress routers.
Benefit A) may be possible to do in a proprietary fashion (althoiugh not preferrable), but B) requires a standard, so that controller-plane can coordinate the gates across multiple routers.